Questionnaire №_____

for bus supports of SHO (P) series for voltage from 35 up to 220 kV

# Postal address and buyer’s details:

Customer___________________________________     ___________________________________________

Town code/telephone _________________________

Fax_______________________________________

Name of the director of the plant _____________________________________________________

Place of installation _______________________________________________________________

Outdoor bus supports of UKHL climatic version for voltage from 35 up to 220kV are intended for supporting wires in alternating current circuits with frequency 50 and 60 Hz.

Working capacity of bus supports is provided in the following conditions:

- upper operating value of ambient air temperature is plus 40°С;

- lower operating value of ambient air temperature is minus 60°С;

- wind speed is no more 40 m/s without icing and no more 15 m/s at icing with ice thickness up to 20 mm.

Seismicity of bus supports is as per MSK-64 scale:

  - with porcelain insulation – 8 points

  - with polymer insulation – 9 points.

Minimum insulators’ failing bending load:

- of porcelain ones - 35-110 kV – 4 kN, 6 kN; 150-220 kV – 6 kN, 8 kN,

- of polymer ones - 35 kV – 5 kN, 110 kV –10 kN, 220 kV – 8 kN.

|  | Parameters | Versions | Order’s value |
| --- | --- | --- | --- |
| 3 | Rated voltage / maximum operating voltage | 35 kV / 40,5 kV |  |
|  |  | 110 kV / 126 kV |  |
|  |  | 150 kV / 172 kV |  |
|  |  | 220 kV / 252 kV |  |
| 4 | Insulation type and specific creepage distance as per GOST 9920 | Porcelain | 1,6 cm/kV |  |
|  |  |  | 2,25 cm/kV |  |
|  |  |  | 2,5 cm/kV |  |
|  |  |  | 3,1 cm/kV |  |
|  |  | Polymer | 2,25 cm/kV |  |
|  |  |  | 2,5 cm/kV |  |
|  | Colour of insulators’ glaze | White |  |
|  |  | Brown |  |
|  | Constructive version | For fastening one wire |  |
|  |  | For fastening two wires |  |
|  | Wire type (indicate) |  |
|  | Order of support pillars for installation | Tube construction of the pillar |  |
|  |  | Built-up construction of the pillar |  |
|  | Height of support pillars | Standard supply: 2856mm (tube), 2816mm (built-up) As per the order: 2200, 2500, 2800, 3000, 3500, 4000, 4500, 5200mm | Under one bus support |  |
|  |  |  | under two bus supports |  |
|  |  |  | under three bus supports |  |
|  | Order of metal structures (as per customer’s sketch) |  |
|  | Order of bus supports for high-frequency barriers’ installation (as per customer’s sketch) |  |
|  | Additional requirements |  |
| 11. | Number of order’s sets |  |

# Text boxes

Manufacturer: CJSC “ZETO”

182100 Pskov region,

Velikie Luki, pr. Oktyabrsky, 79

Telephone (81153) 6-38-10; 6-37-77

Fax (81153) 6-38-45, 6-37-80