Questionnaire №_____ for column SF6 circuit breakers of VGT-110 type

with built-in spring drive

# Postal address and buyer’s details:

Customer___________________________________     ___________________________________________

Town code/telephone _________________________

Fax_______________________________________

Name of the director of the plant ___________________

Place of installation____________________________________________________________________

Circuit breaker is intended for switching operations (closing and opening) and for autoreclosing cycles under given conditions in normal and emergency modes in circuits of three-phase alternating current with 50 Hz frequency and 110 kV rated voltage with earthed neutral.

Circuit breaker consists of three poles (columns) installed on common frame and controlled by one spring drive.

|  | Parameters | Versions | Order’s value |
| --- | --- | --- | --- |
|  | Rated voltage / Maximum operating voltage, kV | 110 / 126 | V |
| 2 | Rated current, А | 2000 |  |
|  |  | 3150 |  |
| 4 | Short-time withstand current / Peak withstand current, kA | 40 / 102 |  |
| 5 | Insulation type (degree of insulation pollution as per GOST 9920) | Porcelain III |  |
|  |  | Porcelain IV (nonstandard supply) |  |
|  | Rated supply voltage of electric motor, V | 400 alternating (three phase) |  |
|  |  | 230 alternating (three phase) |  |
|  |  | 220 direct |  |
|  |  | direct and alternating current motor | 230 alternating (single-phase) 220 direct |  |
| 6) | Rated supply voltage of electromagnets, V | 110 direct |  |
|  |  | 220 direct |  |
| 7) | Adjustment for current of two current release devices | 3 A |  |
|  |  | 5A |  |
| 8) | Order of supports for circuit breaker’s installation (support’s height) | Standard | Fig.2 (2200 mm) |  |
|  |  | As per the order | Indicate height |  |
|  |  | With cantilever, for transformers’ installation | Fig.4 (2220mm |  |
|  |  |  | Indicate height |  |
|  |  | For VMT circuit breakers’ replacement | Fig.3 (678mm) |  |
| 9) | Climatic version as per GOST 15150 | U1 (from plus 40ºC up to minus 45ºC) Insulating medium is SF6 |  |
|  |  | UKHL1* (from plus 40ºC up to minus 55ºC) Insulating medium is mixture of SF6 and CF4 |  |
| 10) | Quantity of additionally delivered SF6 (the first filling is included into supply set) | As per the order (indicate quantity of circuit breaker’s fillings) |  |
| 11) | Extended supply (as per the order), indicate quantity, pcs. | Gas-filling set |  |
|  |  | SF6 leakage detector |  |
|  |  | A device for measuring moisture amount |  |
|  |  | Accounting system of residual commutation life |  |
|  |  | Operating floor of SF6 circuit-breaker with safety cage |  |
| 12) | Additional requirements to circuit breaker |  |
| 13 | Number of circuit breakers in the order |  |

Figure 2 - Рисунок 2

Figure 3 - Рисунок 3

Figure 4 - Рисунок 4

# Text boxes

Manufacturer:

CJSC «ZETO–Gas Technologies»

182100 Pskov region,

Velikie Luki, pr. Oktyabrsky, 79

Tel.: (81153) 6-37-92, 6-37-83,

Fax: (81153) 6-38-45

e-mail: info@zeto.ru

Факс: (81153) 5-16-09